## Slide 1: USING ADC IN ATMEGA32
CSE 315
Courtesy: Muhammad Ali Nayeem, Azad Abdus Salam, Md. Iftekharul Islam Sakib

## Slide 2: LEARNING OBJECTIVE
Why do we need ADC?
What is ADC?
ADC in ATmega32
A simple example

## Slide 3: RECAP
MCU is a digital processor
  Works with binary data
    Just 2 voltage levels
MCU needs to collect information from the real world
  Temperature, Pressure, Humidity, Sound …
    Continuous property
    Infinite possible values
Why do we collect information?
  To analyze the situation
  To take appropriate actions

## Slide 4: RECAP
But how to collect information?
  Sensors: Convert physical property into analog signal
    Voltage, Current, Resistance, …
How can MCU recognize these signal?
  Need to convert into digital data
  How?
    Approximation
  Need something special!

## Slide 5: TYPICAL EMBEDDED APPLICATION

## Slide 6: ADC: QUICK REVIEW

## Slide 7: A-TO-D CONVERSION
Two related steps
Sampling (Approximating the X-axis)
  the analogue signal is extracted at regularly spaced time instants
  the samples have real values
Quantization (Approximating the Y-axis)
  the samples are quantized to discrete levels
  each sample is represented as a binary value

## Slide 8: SAMPLING AN ANALOGUE SIGNAL

## Slide 9: QUANTIZING THE SAMPLED SIGNAL
How many bit to represent the analogue value?
Say, 2 bit to represent analogue value from 0V to 5V
Step size = 5V / 2^2 = 5V / 4 = 1.25V
Digital value = floor(Analogue value / 1.25V)

## Slide 10: QUANTIZING THE SAMPLED SIGNAL

## Slide 11: QUANTIZING THE SAMPLED SIGNAL

## Slide 12: QUANTIZING THE SAMPLED SIGNAL
5v / 8 = 0.625
000
001
010
011
100
111

## Slide 13: 8-BIT ADC

## Slide 14: EXAMPLE

## Slide 15: A QUESTION
What is the difference between an ADC and a digital input pin?

## Slide 16: THE ADC IN ATMEGA32
The ADC has a 10-bit resolution.
  The binary output has n = 10 bits
The ADC has 8 input channels
  Analogue input can come from 8 different sources
  However, it performs conversion on only one channel at a time
If default reference voltage Vref = 5V is used
  step size: 5 V/1024 = 4.88mV
The clock rate of the ADC can be different from the CPU clock rate
  One ADC conversion takes 13 ADC cycles
  An ADC prescaler will decide the ADC clock rate

## Slide 17: RELEVANT PINS

## Slide 18: BLOCK DIAGRAM
ADMUX
ADCSRA
A Sample and Hold circuit
Making sure input voltage is constant during conversion

## Slide 19: MAIN ASPECTS
What are the relevant ADC registers?
  ADMUX
  ADCH/ADCL
  ADCSRA
  SFIOR
What are the steps to use the ADC?
How to use ADC interrupt?

## Slide 20: ADC MULTIPLEXER SELECTION REGISTER (ADMUX)

## Slide 21: SELECTING REFERENCE VOLTAGE VREF
AVCC must not differ more than ±0.3V from VCC.

## Slide 22: ADC RECOMMENDED CONNECTION for Vref = AVCC
https://electronics.stackexchange.com/questions/86207/atmega8-why-do-vcc-and-avcc-have-to-be-connected

## Slide 23: SELECTING INPUT SOURCE

## Slide 24: SELECTING INPUT SOURCE
Why select same ADC source as both positive input and negative input?

## Slide 25: ADC Output
Differential ADC is presented in two’s complement form, from 0x200 (-512d) through 0x1FF (+511d).

## Slide 26: ADCH & ADCL REGISTERS
Why two separate registers?
  Fast read of only one register with a bit of sacrifice on accuracy.
What is the maximum error while reading only ADCH with ADLAR=1?

## Slide 27: Read ADCL Before ADCH
ADCL must be read first, then ADCH, to ensure that the content of the Data Registers belongs to the same conversion.
Once ADCL is read, ADC access to Data Registers is blocked, i.e. value of ADCL and ADCH will not be changed until ADCH is read.
This means that if ADCL has been read, and a conversion completes before ADCH is read, neither register is updated and the result from the conversion is lost.
When ADCH is read, ADC access to the ADCH and ADCL Registers is re-enabled.

## Slide 28: Read ADCL Before ADCH
Can you read only ADCH?
Can you read only ADCL?

## Slide 29: ADC CONTROL AND STATUS REGISTER (ADCSRA)

## Slide 30: ADC CLOCK
250KHz

## Slide 31: STEPS TO USE THE ADC

## Slide 32: SIMPLE EXAMPLE

## Slide 33: SIMPLE EXAMPLE

## Slide 34
What if you want to do some other work while ADC going on?
float voltage = (ADCH << 2) * 5 / 1024;

## Slide 35: SIMPLE EXAMPLE: USING ADC INTERRUPT

## Slide 37: TEMPERATURE SENSOR

## Slide 38: TEMPERATURE SENSOR

## Slide 39: INTERFACING LM34 TO AVR

## Slide 40: INTERFACING LM34 TO AVR
If we use the internal 2.56 V reference voltage
  step size would be 2.56 V/1024 = 2.5 mV
  This makes the binary output of the ADC four times the real temperature
  Divide the binary output by 4 to get the real temperature

## Slide 41: INTERFACING LM34 TO AVR

## Slide 42: INTERFACING LM34 TO AVR
#include <avr/io.h> //standard AVR header
int main (void)
{
  DDRB = 0xFF; //make Port B an output
  ADCSRA = 0x87; //make ADC enable and select ck/128
  ADMUX = 0xE0; //2.56 V Vref and ADCO single-ended
  //data will be left-justified
  while (1 ){
    ADCSRA |= (l<<ADSC); //start conversion
    while((ADCSRA & (l<<ADIF))==0); //wait for end of conversion
    PORTB = ADCH; //give the high byte to PORTB
  }
  return 0;
}

## Slide 43: SPECIAL FUNCTION IO REGISTER (SFIOR)

## Slide 44: AUTO TRIGGER LOGIC

## Slide 45: AUTO TRIGGER SOURCE

## Slide 46: TIMER: NORMAL VS. CTC MODE

## Slide 47: A PRACTICAL PROBLEM
We need to sample an analog signal @ 20 kHz sampling frequency
The only way to do this correctly
  use auto-triggering with exact time intervals
Let’s see how can we do this using Timer0

## Slide 48: SOLUTION OVERVIEW
Assume
  system clock frequency = 16 MHz
  Timer0 prescaler = 8
To ensure 20 kHz sampling frequency
  Time between successive ADC conversions?
    50us
  Use Timer0 to trigger ADC every 50us
  How to trigger Timer0 compare match every 50us?
    Need to count?
      50us/(8/16000000) = 100
      From 0 to 99
      Set OCR0 = 99

## Slide 49: SOLUTION OVERVIEW
  Timer0 compare match trigger every 50us
    Need to count?
    50us/(8/16000000) = 100
    From 0 to 99
    Set OCR0 = 99
    Why 99 instead of 100 ?

## Slide 50: SOLUTION OVERVIEW
Now let’s select ADC prescaler properly
  ADC conversion must be completed before next Timer0 compare match occur
One auto triggered ADC conversion time takes 13.5 ADC cycles

## Slide 51: SOLUTION OVERVIEW
Now let’s select ADC prescaler properly
  ADC conversion must be completed before next Timer0 compare match occur
One auto triggered ADC conversion time takes 13.5 ADC cycles

## Slide 52: SOLUTION OVERVIEW
To fit in to 50us window we can select prescaller up to 32
Gives enough time to
  Complete auto triggered ADC cycle
  Clear Timer0 compare match flag
  Store ADC value within one sample period
  …

## Slide 53: SOLUTION OVERVIEW
ADC prescaller = 32
Gives enough time to
  Complete auto triggered ADC cycle
  Clear Timer0 compare match flag
  Store ADC value within one sample period
  …

## Slide 54: COMPLETE CODE FOR ATMEGA328
http://www.embedds.com/adc-on-atmega328-part-2/